## Slide 1: Lock Out Tag Out Review
KNOW &
UNDERSTAND
YOUR COMPANY’S
LOCK-OUT TAG
OUT PROCEDURES

## Slide 2: Lock Out Tag Out Review
Prior to working in, on, or around any equipment, machine, process, or operation where there is a hazard from activation of electrical, thermal, hydraulic, chemical, radiation or stored sources of energy, the equipment, machine, process or operation will be secured against unexpected movement and/or exposing miners to other hazards involving these sources of energy.

## Slide 3: Lock Out Tag Out Review
Lock Out/Tag Out Procedures
 Notify “affected” employees and any employees
working nearby.
 Shut down the equipment.
 Identify all energy sources and possible hazards.
 Disconnect the power.
 Lock-Out/Tag Out equipment.
 Neutralize other possible energy sources.
- Lower all suspended parts.
- Block movable parts.
- Drain or bleed hydraulic lines to remove pressure.
- Release or block spring energy.
- Secure machine parts to be sure they can’t move
or fall unexpectedly.
- Drain capacitors and other sources of stored energy.
 Test Equipment (if not energized). Perform service/
maintenance.
 Push start buttons (Twice). Return to “off” or neutral
position.
Test Electric Circuits. (Only a “Certi ed” Person can do this.)
 After Completion, before starting work, double check
everything.
Equipment – In operating condition. (Controls are in neutral.)
Guards – In place.
Tools – removed.
 Braces, pins, blocks, chains – removed.
Work Area – Cleared.
Personnel – Out of Danger Zone.
 Affected persons notified of startup.
 Tags and locks – removed by the authorized persons
who installed them.
 Reenergize.

## Slide 4: Lock Out Tag Out Review
The West Virginia Office of Miners health, Safety & Training have suspended twelve electrical certifications since September of 2019.
These suspensions all involve failure to lock and tag energized equipment.