## Slide 1: Methane (CH4)
Specific Gravity: 0.5545
Explosive Range and Flammability:
Methane is flammable.
Its explosive range is 5 to 15 percent when there is at least 12.1 percent oxygen.
Methane is most explosive, however, in the 9.5 to 10 percent range.
Notes: Note: Methane does not occur in all metal/nonmetal mines; however it does occur in mines such as salt, oil shale, and trona mines.
Use this lecture material only if methane is a possible gas in the mine or mines in which the team will be working.

## Slide 2: Methane (CH4)
Explosive Range (5% to 15%) and Flammability:
  Methane's explosive range is not an absolute measure of safety.
  There are other important factors to take into consideration.
  For example, the presence of other combustible gases with wider explosive ranges or lower ignition points than methane may result in a more highly explosive mixture.

## Slide 3: Methane (CH4)
Health Hazards: Methane is not toxic. In high concentrations, however, it can cause asphyxiation by lowering the oxygen content of normal air. The most dangerous aspect of methane is the fact that it is explosive.
Solubility: Slightly soluble in water.
Color/Odor/Taste: Colorless, odorless, tasteless.

## Slide 4: Methane (CH4)
Cause or Origin:
  Methane may be liberated from the strata in metal/nonmetal mines when carbonaceous shale is penetrated, and occasionally when carbonaceous rock is contacted or is in the vicinity.
  Methane can issue in large quantities from sudden outbursts or from feeders or blowers or clay veins in some mines.
  Methane can also be liberated by the decomposition of timbers and when water is removed from the mine.

## Slide 5: Methane (CH4)
Where Found:
  Because methane is relatively light, it collects in high places, so you can expect to find it near the roof of the mine.
  You also may find it at freshly mined areas, in poorly ventilated areas, and in abandoned or unused sections of the mine, especially where timbering is extensive.
  Because it is a relatively light gas (low specific gravity), methane is usually easy to disperse and remove from the mine by means of ventilation.

## Slide 6: Methane (CH4)
Detection Methods: To test for methane, use a methane detector or chemical analysis. Remember that methane is a light gas; so hold your portable detector high.
Notes: Note: Point out to the team that if a detector indicates the presence of methane, this may need further analysis. Detectors that use the Wheatstone Bridge Principal, for example, will give a positive reading in the presence of any combustible gas (including methane). The Riken detector, on the other hand, does not distinguish CO2 from methane.

## Slide 7: Methane (CH4)
Where to Test: In mines where methane is possible, test as often as necessary during exploration to determine the methane content of the surrounding atmosphere. Also test for methane when normal ventilation is disrupted and when you are entering abandoned workings or removing water from old workings.
  Tests to be made at least 12 inches from roof, face, ribs, and floor

## Slide 8: Methane (CH4)
Meaning of Findings: If methane is present, it's important to monitor it carefully because it is potentially explosive if there is enough oxygen present. If methane exists in potentially explosive concentrations or in combination with other gases that extend its explosive range.

## Slide 9
Tests to be made at least 12 inches from roof, face, ribs, and floor
Working places, intake air courses (includes belt entries), areas where equipment is being installed or removed
Testing shall be done before equipment is energized, taken into or operated in a working place.
Every 20 minutes during operation of equipment or when operations has stopped for more than 20 minutes.
If any explosive gas of 1% or more is found in the place, electrical equipment shall not be taken into that place.
Methane of 1% or more, the power shall be removed from the machine and ventilation corrected.
Methane of 1.5% or more, the section power shall be removed and men evacuated. Only those correcting ventilation shall remain.
Test for Methane
(CH4)